## Slide 1: Inter-AS MPLS Services

## Slide 2: AGENDA
MPLS L3 VPN - short recap
Inter-AS L3 VPN
MPLS L2 VPN - short recap
Inter-AS L2 VPN

## Slide 3: MPLS Services Spanning Multiple SP Networks
Service Provider #1
AS100
VPN-X
VPN-Z1
VPN-Z2
Service Provider #2
AS200
CE
CE
CE
CE
CE
CE
PE
PE
PE
PE
PE
Customer
WAN
ASBR
ASBR
MPLS Services - provisioned over multiple
Autonomous Systems

## Slide 4: Inter-AS VPN - Stitching VPNs Together …
VPN-110
VPN-120
VPN-130
VPN-999
VPN-210
VPN-220
VPN-230
VPN-888
X
CN-10
CN-20
CN-30
CN-99
CN-10
CN-20
CN-30
CN-99

## Slide 5: Carrier Supporting Carrier - Carrying VPNs Transparently
Partner carrier
VPN-110
VPN-120
Partner carrier
VPN-110
VPN-120
CsC network
VPNs are not stitched to each other.
Rather, the CsC network acts as a (MPLS) tunnel for all LSPs.
The CsC does not interfere with any services in their partner carrier networks.
ALL VPNs are carried transparently over the combined E2E MPLS LSP

## Slide 6: MPLS L3 VPN Recap

## Slide 7: MPLS in One Slide
VPN-A
VPN-A
VPN-B
VPN-B
E
T
H
I
PH
DATA
E
T
H
I
PH
DATA
VP
L
T
L
Label
stack
E
T
H
I
PH
DATA
E
T
H
I
PH
DA
T
A
VP
L
T
L
E
T
H
I
PH
DATA
MPLS Domain
(CORE)
P
P
PE
PE
PE
CE
CE
CE
Provider Edge
(EDGE)
FP: Label swap
CP: Signaling, TE/FRR ...
Service-agnostic
(e.g. BGP-free)
FP: Label push/pop + IP forw
CP: Routing (BGP/IGP) and Service Termination (e.g. L2/L3 VPN)
FP: IP forwarding
CP: Routing (BGP/IGP)
Access
DSLAM
CMTS
etc.
Access
Aggregation!

## Slide 8: L3 VPN - Recap ...
CE
P
P
PE
PE
CE
CE
CE
PE
VPN A
VPN A
VPN B
VPN B
10.12.0.0/16
10.13.0.0/16
10.12.0.0/20
10.11.224.0/19
Overlapping IP ranges!
Normal in the VPN world.
Service Provider network needs to take care of it ...

## Slide 9: Overlapping IP Address Space - Route Distinguisher
CE
P
P
PE
PE
CE
CE
CE
PE
VPN A
VPN A
VPN B
VPN B
10.12.0.0/16
10.13.0.0/16
10.12.0.0/20
10.11.224.0/19
Overlapping IP ranges!
65000:111
65000:222
Solution
Route Distinguisher - 64-bit ID
prepended to IPv4 prefixes
locally defined on EACH PE

## Slide 10: VPN-IPv4 NLRI Format
VPN-IPv4 address family
  New BGP-4 subsequent address family identifier (SAFI 128)
    Consists of MPLS label + route distinguisher + subscriber IPv4 prefix
  Route distinguisher disambiguates IPv4 addresses
    Allows service provider to administer its own numbering space
VPN-IPv4 addresses are distributed by MP-BGP
  Uses multiprotocol extensions for BGP4 (RFC 4760)
A /32 IPv4 prefix produces a VPN-IPv4 prefix with a mask of /120 (15 octets)
  The Junos OS CLI displays only show IPv4 prefix length (that is, /32)
Route Distinguisher
Type
Administrator
Assigned Number
Subscriber IPv4 Prefix
(2 bytes)
(variable length)
(variable length)
(0–4 bytes)
MPLS Label
(3 bytes)
Mask
(1 byte)

## Slide 11: Redistribution of Prefixes - MP-iBGP
CE
P
P
PE
PE
CE
CE
CE
PE
VPN A
VPN A
VPN B
VPN B
10.13.0.0/16
10.11.224.0/19
10.12.0.0/20
65000:111
10.12.0.0/16
65000:222
65000:111:10.12.0.0/20
65000:222:10.12.0.0/16
65000:111:10.12.0.0/20
65000:222:10.12.0.0/16
BGP
BGP
65000:101
65000:22
RDs for the same VPN MAY DIFFER from PE to PE!
How to ensure that prefixes rcv'd by BGP end up in the right VPN Routing Table (VRF)?

## Slide 12: Route Target - in which VPN to Install the Route?
CE
P
P
PE
PE
CE
CE
CE
PE
VPN A
VPN A
VPN B
VPN B
10.13.0.0/16
10.11.224.0/19
65000:111:10.12.0.0/20
RT: 65000:1
65000:222:10.12.0.0/16
RT: 65000:2
10.12.0.0/20
VPN-IMPORT policy:
if (RT==65000:2):
vpn = VPN_B
VPN-IMPORT policy:
if (RT==65000:1):
vpn = VPN_A
10.12.0.0/16

## Slide 13: MP-BGP Packet Under the Engine Hood
VPNv4 Prefix 1:1:200.1.62.4/30 ; Label = 23
Route Target = 3:3

## Slide 14: Route Target Extended Community
Each VPN-IPv4 route advertised through MP-BGP is associated with a route target community
  Export policy or explicit configuration define the targets associated with routes a PE router sends
Upon receipt of a VPN-IPv4 route, a PE router decides whether to add that route to a VRF table
  Import policies or explicit configuration define which routes to add to a given VRF table
Route isolation between VRF tables is accomplished through careful policy administration
  Service provider provisioning tools can determine the appropriate export and import targets automatically

## Slide 15: MPLS L3 VPN Operation - Summary
S: 10.1.12.10
D: 10.2.34.30
IP packet
VPN Label
Trans. label
T-Label swap
Penltimate POP Hopping
(PHP)
VPN Label

## Slide 16: Hierarchical MPLS Services - Model Summary
Customer
Site 1
Customer
Site 2
PE-C1
ASBR
PE-C2
LSP
LSP
MPLS L2/L3 VPN
MPLS L2/L3 VPN
ASBR
Provider 1
Provider 2
Service Provider
(Carrier of Carriers)
SP (Carrier) Island #1
SP (Carrier) Island #2
PE12
PE11
PE21
PE22
PE1
PE2
P
LSP
LSP
P2
P1
LSP
E2E LSP
Customer
Site 1
Customer
Site 2
Inter-provider VPN
Carrier supporting Carriers (CsC)

## Slide 17: Inter-AS MPLS L3 VPN

## Slide 18: Inter-AS MPLS L3 VPN
Stitching VPNs sitting in two networks to each other.
RFC4364 - Chapter 10 - discusses 3 options:
  Option A - uses dedicated VLAN (groups) per VRF on ASBR-ASBR link
  Option B - uses MP-EBGP session to exchange VPNv4 routers + VPN labels
  Option C - uses BGP-LU to create a seamless MPLS domain with E2E LSPs (and RR-to-RR MP-EBGP multihop session to exchange VPNv4 routers + VPN labels)

## Slide 19: Inter-AS VPN - Option A
Basic Idea - ASBR-2 behaves like a CE to the ASBR-1 (and vice versa):
  On ASBRs - SP-1 and SP-2 provision all VPNs they want to share with each other.
  Two ASBRs connect with a trunk (tagged Ethernet port) - one VLAN per VRF.
  On each VLAN, within the VRFs - SP-1 and SP-2 configure a BGP session.
  This BGP session behaves like a standard PE-CE session.
  There is no MPLS-labeled traffic on the trunk
P-1
PE-1
P-2
PE-2
SP 1
SP 2
VPN B
Site 1
ASBR-1
ASBR-2
VPN A
Site 1
VPN A
Site 2
VPN B
Site 2
VPN C
Site 1
VPN C
Site 2
IEEE 802.1Q
TRUNK
ONE VLAN
per each VRF

## Slide 20: Inter-AS VPN - Option A - MPLS Domain Limits
P-1
PE-1
P-2
PE-2
SP 1
SP 2
VPN B
Site 1
ASBR-1
ASBR-2
VPN A
Site 1
VPN A
Site 2
VPN B
Site 2
VPN C
Site 1
VPN C
Site 2
IEEE 802.1Q
TRUNK
ONE VLAN
per each VRF
MPLS
domain
MPLS
domain
IP (non-MPLS)
domain

## Slide 21: Inter-AS VPN - Option A - Detailed Operation
BGP
IPv4
MP-iBGP
VPNv4
LDP
BGP
IPv4
MP-iBGP
VPNv4
RSVP
BGP
IPv4
Pure IP
(no labels!)
S: 10.1.12.10
D: 10.2.34.30
VPN-L 302016
T-L 349184
S: 10.1.12.10
D: 10.2.34.30
VPN-L 301008
T-L 300048

## Slide 22: Inter-AS Option A - Configuration Excerpts
interfaces {
ge-0/0/9 {
description "private99: mm1 -- mm3";
flexible-vlan-tagging;
encapsulation flexible-ethernet-services;
unit 110 {
vlan-id 110;
family inet {
address 100.15.110.1/24;
}
family inet6 {
address 2001:100:15:110::1/64;
}
}
unit 120 {
vlan-id 120;
family inet {
address 100.15.120.1/24;
}
}
...
}
}
routing-instances {
VPN-110 {
instance-type vrf;
interface ge-0/0/9.110;
route-distinguisher 100.0.0.1:110;
protocols bgp {
group ebgp-vpn {
peer-as 200;
neighbor 100.15.110.2;
}
group ebgp-vpnv6 {
peer-as 200;
neighbor 2001:100:15:110::2;
}
}
}
VPN-120 {
instance-type vrf;
interface ge-0/0/9.120;
route-distinguisher 100.0.0.1:120;
protocols bgp {
group ebgp-vpn {
peer-as 200;
neighbor 100.15.120.2;
}
}
}
}

## Slide 23: Demo Topology
Loopbacks (lo0):
IPv4: 100.0.0.X/32
IPv6: 2001:100::X/128
Point-to-point links:
IPv4: 100.8.Y.0/30
IPv6: 2001:100:8:Y::/64
Loopbacks (lo0):
IPv4: 200.0.0.X/32
IPv6: 2001:200::X/128
Point-to-point links:
IPv4: 200.8.Y.0/30
IPv6: 2001:200:8:Y::/64
cr1
cr2
pe1
pe2
ace
mm1
mm3
mm4
cr3
cr4
pe3
pe4
mm2
bce
AS100
AS200
.1
.2
.3
.4
.5
.6
.1
.2
.3
.4
.5
.6
IEEE 802.1Q
trunks
rr1
rr2
.11
.11
sv8-pod4-vmm:/homes/btodorovic/vmm_config/inter-as-vpn/

## Slide 24: Inter-AS VPN Option A - Pro et Contra
PRO
Simple to understand by low-skilled techies.
Simple to administer (one VLAN per VPN)
Easy to troubleshoot (no MPLS on the trunk)
Per-VLAN QoS.
Per-VLAN IP filtering (pure IP packets)
CONTRA
ASBR requires 1000s of VRF definitions
  This can be automated, though ...
Capacity management - required per VRF
  e.g. BGP local-preference per each VRF to define primary/backup NNI for traffic
VLANs - limited to 4094, although ...
  QinQ (stacked VLANs) expand this to ~16M
Logical interface limitations - in Junos
  128,000 IFLs per chassis, AND:
  16,380 IFLs per each IFD (physical interface)

## Slide 25: Inter-AS VPN - Option B
Basic Idea - VPNs advertised E2E, but each domain has separate LSPs:
  ASBR-1 advertises VPN Labels for each VPN in SP-1 - via MP-EBGP
  ASBR-2 advertises VPN Labels for each VPN in SP-2 - via MP-EBGP
Single link, single EBGP session, no VLANs
VPN selection - performed by BGP route filtering (policies).
P-1
PE-1
P-2
PE-2
SP 1
SP 2
VPN B
Site 1
ASBR-1
ASBR-2
VPN A
Site 1
VPN A
Site 2
VPN B
Site 2
VPN C
Site 1
VPN C
Site 2
MP-EBGP

## Slide 26: Inter-AS VPN - Option B - MPLS Domain Limits
P-1
PE-1
P-2
PE-2
SP 1
SP 2
VPN B
Site 1
ASBR-1
ASBR-2
VPN A
Site 1
VPN A
Site 2
VPN B
Site 2
VPN C
Site 1
VPN C
Site 2
MPLS
domain
MPLS
domain
VPN-v4
MPLS-enabled link
required to carry VPN label
information, but transport
labels are still qeparated
ONE IP LINK
(NO VLANs!)

## Slide 27: Inter-AS VPN - Option B - Detailed Operation
BGP
IPv4
MP-iBGP
VPNv4
LDP
MP-eBGP
VPNv4
MP-iBGP
VPNv4
RSVP
BGP
IPv4
VPN labels
advertised
via EBGP!
S: 10.1.12.10
D: 10.2.34.30
VPN-L 302016
T-L 349184
S: 10.1.12.10
D: 10.2.34.30
VPN-L 301008
T-L 300048

## Slide 28: Inter-AS Option B - Configuration Excerpts
interfaces {
ge-0/0/9 {
description "private99: mm1 -- mm3";
unit 0 {
family inet {
address 100.15.1.1/24;
}
family inet6 {
address 2001:100:15:1::1/64;
address ::ffff:100.15.1.1/126;
}
family mpls;
}
}
}
protocols {
mpls {
interface ge-0/0/9.0;
}
}
protocols {
bgp {
group inter-as {
import rt-update;
family inet-vpn {
unicast;
}
family inet6-vpn {
unicast;
}
peer-as 200;
neighbor 100.15.1.2;
}
}
}
policy-options {
policy-statement rt-update {
term VPN-110 {
from community RT-VPN-110-REMOTE;
then {
community add RT-VPN-110;
}
}
term VPN-120 {
from community RT-VPN-120-REMOTE;
then {
community add RT-VPN-120;
}
}
term VPN-130 {
from community RT-VPN-130-REMOTE;
then {
community add RT-VPN-130;
}
}
}
}

## Slide 29: Demo Topology
Loopbacks (lo0):
IPv4: 100.0.0.X/32
IPv6: 2001:100::X/32
Point-to-point links:
IPv4: 100.8.Y.0/30
IPv6: 2001:100:8:Y::/64
Loopbacks (lo0):
IPv4: 200.0.0.X/32
IPv6: 2001:200::X/32
Point-to-point links:
IPv4: 200.8.Y.0/30
IPv6: 2001:200:8:Y::/64
cr1
cr2
pe1
pe2
ace
mm1
mm3
mm4
cr3
cr4
pe3
pe4
mm2
bce
AS100
AS200
.1
.2
.3
.4
.5
.6
.1
.2
.3
.4
.5
.6
rr1
rr2
.11
.11
EBGP-MH
IPv4
EBGP-MH
IPv4

## Slide 30: Inter-AS VPN Option B - Pro et Contra
PRO
One single BGP session for all VRFs
VRF selection can be performed by route policies, filters etc.
Transport MPLS networks still separated from each other - only VPN labels exchanged.
CONTRA
Difficult per-VRF QoS control (requires mostly MF-filters)
Difficult IP packet filtering (labeled packets)
No E2E LSP - LSP broken on the ASBRs

## Slide 31: Inter-AS VPN - Option C ("Seamless MPLS")
Basic Idea - E2E LSP among all PEs in both SP-1 and SP-2 networks!
Seamless MPLS transport - E2E LSPs signaled using EBGP-LU between ASBRs
VPN signaling - provided by MP-EBGP (multihop) sessions between RRs
P-1
PE-1
P-2
PE-2
SP 1
SP 2
VPN B
Site 1
ASBR-1
ASBR-2
VPN A
Site 1
VPN A
Site 2
VPN B
Site 2
VPN C
Site 1
VPN C
Site 2
RR-2
RR-1
MP-EBGP - multihop + NH-unchanged
AFI=1 / SAFI=128
EBGP-LU
AFI=1 / SAFI=4
E2E LSP
(signaled by EBGP-LU)
MPLS L3 VPNs
(signaled by MP-EBGP-MH)

## Slide 32: Inter-AS VPN - Option C - MPLS Domain Limits
P-1
PE-1
P-2
PE-2
SP 1
SP 2
VPN B
Site 1
ASBR-1
ASBR-2
VPN A
Site 1
VPN A
Site 2
VPN B
Site 2
VPN C
Site 1
VPN C
Site 2
E2E LSPs create a virtually
single common MPLS domain
ONE IP LINK
(NO VLANs!)

## Slide 33: Inter-AS VPN - Option C - Detailed Operation
BGP
IPv4
iBGP-LU
Labels
LDP
eBGP-LU
RR
RR
MP-eBGP-MH
VPNv4
RSVP
MP-iBGP
VPNv4
MP-iBGP
VPNv4
iBGP-LU
Labels
BGP
IPv4

## Slide 34: Inter-AS Option C - Juniper Networks Implementation
Two ways to implement:
Use inet.3 as BGP-LU primary RIB - using the knob rib inet.3 in the BGP-LU configuration Junos instructs BGP-LU to store advertised/received NLRI into inet.3 instead of inet.0.
Copy BGP-LU prefixes from inet.0 to inet.3 - the default BGP RIB inet.0 is used to store advertised and received BGP-LU NLRI; however, using the knob resolve-vpn, BGP-LU process is instructed to keep copying all its prefixes into inet.3.
Both methods provide the same effect and they are equally being used.

## Slide 35: Inter-AS Option C - Configuration Excerpts
interfaces {
ge-0/0/9 {
description "private99: mm1 -- mm3";
unit 0 {
family inet {
address 100.15.1.1/24;
}
family mpls;
}
}
}
protocols {
mpls {
interface ge-0/0/9.0;
}
}
routing-options {
interface-routes {
rib-group inet RG-LOCAL-LOOPBACKS;
}
rib-groups {
RG-LOCAL-LOOPBACKS {
import-rib [ inet.0 inet.3 ];
import-policy PL-MY-LOCAL-LOOPBACK;
}
RG-REMOTE-LOOPBACKS {
import-rib [ inet.3 inet.0 ];
import-policy PL-REMOTE-LOOPBACKS;
}
}
}

## Slide 36
protocols {
bgp {
group rr {
type internal;
local-address 100.0.0.1;
export lu-int;
family inet {
unicast;
labeled-unicast {
rib-group RG-REMOTE-LOOPBACKS;
aigp;
rib {
inet.3;
}
}
}
}
group ebgp-lu {
type external;
export lu-ext;
family inet {
labeled-unicast {
aigp;
rib {
inet.3;
}
}
}
peer-as 200;
neighbor 100.15.1.2;
}
}
}
policy-options {
policy-statement lu-int {
term MY-LOOPBACK {
from {
protocol direct;
rib inet.3;
route-filter 100.0.0.0/24 prefix-length-range /32-/32;
}
then {
metric 0;
next-hop self;
accept;
}
}
term BGP {
from {
protocol bgp;
rib inet.3;
}
then {
next-hop self;
accept;
}
}
then reject;
}
}

## Slide 37
protocols {
bgp {
group rr {
type internal;
local-address 100.0.0.1;
export lu-int;
family inet {
unicast;
labeled-unicast {
rib-group RG-REMOTE-LOOPBACKS;
aigp;
rib {
inet.3;
}
}
}
}
group ebgp-lu {
type external;
export lu-ext;
family inet {
labeled-unicast {
aigp;
rib {
inet.3;
}
}
}
peer-as 200;
neighbor 100.15.1.2;
}
}
}
policy-options {
policy-statement lu-ext {
term LOOPBACKS {
from {
protocol [ direct bgp ];
rib inet.3;
route-filter 100.0.0.0/24 prefix-length-range /32-/32;
}
then {
next-hop self;
accept;
}
}
}
}

## Slide 38
protocols {
bgp {
group ebgp-mh {
type external;
multihop {
ttl 255;
no-nexthop-change;
}
local-address 100.0.0.11;
import rt-update;
family inet {
unicast;
}
family inet-vpn {
unicast;
}
family inet6 {
labeled-unicast;
}
family inet6-vpn {
unicast;
}
family l2vpn {
signaling;
}
peer-as 200;
neighbor 200.0.0.11;
}
}
}
policy-options {
policy-statement rt-update {
term VPN-110 {
from community RT-VPN-110-REMOTE;
then {
community add RT-VPN-110;
}
}
term VPN-120 {
from community RT-VPN-120-REMOTE;
then {
community add RT-VPN-120;
}
}
term VPN-130 {
from community RT-VPN-130-REMOTE;
then {
community add RT-VPN-130;
}
}
}
}

## Slide 39: Demo Topology
Loopbacks (lo0):
IPv4: 100.0.0.X/32
IPv6: 2001:100::X/32
Point-to-point links:
IPv4: 100.8.Y.0/30
IPv6: 2001:100:8:Y::/64
Loopbacks (lo0):
IPv4: 200.0.0.X/32
IPv6: 2001:200::X/32
Point-to-point links:
IPv4: 200.8.Y.0/30
IPv6: 2001:200:8:Y::/64
cr1
cr2
pe1
pe2
ace
mm1
mm3
mm4
cr3
cr4
pe3
pe4
mm2
bce
AS100
AS200
.1
.2
.3
.4
.5
.6
.1
.2
.3
.4
.5
.6
rr1
rr2
.11
.11
EBGP-LU
EBGP-LU
MP-EBGP Multihop

## Slide 40: Inter-AS VPN Option C - Pro et Contra
PRO
One single BGP session for all VRFs (centrally controlled - on the RRs)
VRF selection can be performed by route policies, filters etc.
E2E LSPs - provide seamless connectivity for both L2 and L3 VPNs
Capacity management - flexible, because of E2E LSPs
CONTRA
Difficult per-VRF QoS control (requires mostly MF-filters)
Difficult IP packet filtering (labeled packets)
Difficult to understand (but easy to maintain)

## Slide 41: Carrier Supporting Carrier - Carrying VPNs Transparently
Partner carrier
VPN-110
VPN-120
Partner carrier
VPN-110
VPN-120
CsC network
VPNs are not stitched to each other.
Rather, the CsC network acts as a (MPLS) tunnel for all LSPs.
The CsC does not interfere with any services in their partner carrier networks.
ALL VPNs are carried transparently over the combined E2E MPLS LSP

## Slide 42: CsC == Extension of Inter-AS Option C
Actually, not that complex as it sounds - just Inter-AS Option C, extended ...
VPN signaling - still provided by MP-EBGP (multihop) sessions between endpoint RRs
E2E LSPs - signaled between SP-1, CsC and SP-2 domain using EBGP-LU
P-1
PE-1
P-2
PE-2
SP 1
SP 2
VPN B
Site 1
ASBR-1
ASBR-2
VPN A
Site 1
VPN A
Site 2
VPN B
Site 2
VPN C
Site 1
VPN C
Site 2
RR-2
RR-1
E2E LSP
(signaled by EBGP-LU)
ASBR-3
ASBR-4
P-3
EBGP-LU
AFI=1 / SAFI=4
EBGP-LU
AFI=1 / SAFI=4
MP-EBGP - multihop
AFI=1 / SAFI=128
SP 3 (CsC)

## Slide 43: MPLS L2 VPN Recap

## Slide 44: Taxonomy of L2 VPN Services
Any-to-Any
Ethernet Wire Service
- IETF: pseudo-wire (PWE) service
- MEF: E-Line service
- Juniper: VPWS / L2VPN / L2CKT
Ethernet LAN Service
- IETF: VPLS
- MEF: E-LAN service
- Juniper: VPLS
L2 VPN
Point-to-Point

## Slide 45: In a Nutshell
45
Any-to-Any
(VPLS / E-LAN)
Point-to-point
inter-regional
(VPWS / E-LINE)
Point-to-point
intra-regional
(VPWS / E-LINE)

## Slide 46: MPLS L2 VPN - Full Taxonomy
Point-to-point L2 VPNs (a.k.a. pseudowires / VPWS / E-LINE) - may be:
  BGP-signaled (a.k.a. Kompella) - RFC6624
  LDP-signaled (a.k.a. Martini) - RFC8077
Any-to-any L2 VPNs (VPLS / E-LAN) - may be:
  BGP-signaled (a.k.a. K. Kompella) - RFC4761
  LDP-signaled (a.k.a. Laserre - V. Kompella) - RFC4762
  LDP-signaled with BGP auto-discovery - RFC6074
EVPN (EVPN - new standard, based on the packet forwarding based on the MAC address lookups):
  EVPN - BGP MPLS-based Ethernet VPN - RFC7432
  Provider Backbone Bridging Combined with EVPN (PBB-EVPN) - RFC7623
RFC4448 - Encapsulation Methods for Transport of Ethernet over MPLS Networks
Defines the common forwarding plane for all L2VPN flavors

## Slide 47: Pseudowire - L2 Tunnel Between CEs
47
Pseudo-Wire
Customer Devices
MPLS Backbone
PE-POP
PE-POP
CE
CE
Customer Devices
Pseudowire
Emulates a P2P connection
between two sites

## Slide 48: Pseudowire - a Closer Look
MPLS
AMS-001
MPLS edge router
BRU-001
MPLS edge router
VLAN ID 1004
(SP tag - NL)
ge-1/0/0.1004
ge-0/2/1.2003
VLAN ID 2003
(SP tag - BE)
Customer
PILOT - NL
NNI
UNI
Access
Network
Provider
Access
CE
Access
PE
Access Network NL
Customer
PILOT - BE
UNI
NNI
Access Network Provider
Access
CE
Access
PE
Access Network BE
MPLS Backbone
?

## Slide 49: RFC 4448 - Ethernet MPLS Encapsulation
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
EXP
TTL (set to 2)
1
PW Label
Control Word (optional)
Inner Label
EXP
TTL
0
PSN Tunnel Label (LDP or RSVP)
Outer Label
Layer-2 PDU
Original Ethernet
frame
(including VLAN tags!)
TCI
TPID
<2 octets>
<2 octets>
Ethertype
SA
DA
Data
<6 octets>
<2 octets>
<46-1500>
<6 octets>

## Slide 50: L2 Circuit - Control and Forwarding Plane - Principle
MPLS Backbone
NNI
NNI
AMS-001
MPLS edge router
BRU-001
MPLS edge router
VLAN ID 1004
(SP tag - NL)
ge-1/0/0.1004
ge-0/2/1.2003
VLAN ID 2003
(SP tag - BE)
Control Plane - LDP
(T-LDP session PE1-PE2)
SA
DA
DATA
1004
0x9100
Qc
SA
DA
DATA
2003
0x8100
Qc
SA
DA
DATA
1004
0x9100
Qc
PWL
TL1
SA
DA
DATA
1004
0x9100
Qc
PWL
TLn
SA
DA
DATA
1004
0x9100
Qc
PWL
TL2
?!
PE1
P
PE2
Outer Label
Swap

## Slide 51: VPLS - a Huge Learning Bridge
51
Pseudo-Wire
Ethernet Tagstacking/VLAN
CPE Router/Switch
CPE Router/Switch
CPE Router/Switch
CPE Router/Switch
MPLS Backbone
PE-POP
PE-POP
PE-POP
PE
PE-CLE
PE-CLE
PE-CLE

## Slide 52: VPLS Example
Service
Provider
Network
Customer
PILOT - NL
Customer
PILOT - BE
UNI-N
UNI-C
UNI-C
UNI-N
ACCESS
ACCESS
ACCESS
CE
ACCESS
CE
ACCESS
PE
ACCESS
PE
VLAN ID 1004
(SP tag - NL)
ge-1/0/0.1004
ge-0/2/1.2003
VLAN ID 2003
(SP tag - BE)
ACCESS NETWORK NL
ACCESS NETWORK BE
Customer
PILOT - FR
UNI-N
UNI-C
ACCESS
ACCESS
CE
ACCESS
PE
ACCESS NETWORK FR
Customer
PILOT - DE
UNI-C
ACCESS
ACCESS
CE
ACCESS
PE
ACCESS NETOWRK DE
VLAN ID 3002
(SP tag - FR)
ge-0/2/0.3002
VLAN ID 4001
(SP tag - DE)
ge-0/3/0.4001
UNI-N
Pseudowire mesh (T-LDP)

## Slide 53: Inter-AS MPLS L2 VPN

## Slide 54: Inter-AS L2 VPN - Challenges
MPLS L3 VPNs - control plane is provided by BGP.
MPLS L2 VPNs - have two ways to signal reachability information:
  LDP
  BGP
BGP-signaled L2 VPNs - we can (in theory) reuse Options A/B/C
  This strongly depends on the vendor, s/w version and features supported.
  Junos - supports Inter-AS VPWS and VPLS - Options A/B/C
LDP-signaled L2 VPNs - there are two options available:
  L2VPN "stitching" on the interconnect ("Option A" equivalent)
  T-LDP sessions over BGP-LU-signaled E2E LSPs ("Option C" equivalent).

## Slide 55: Inter-AS L2 VPN - "Option A" (Stiched PWs)
Basic Idea - ASBR-2 behaves like a CE to the ASBR-1 (and vice versa):
  On ASBRs - SP-1 and SP-2 terminate all L2 VPNs they want to share with each other.
  Two ASBRs connect with a trunk (tagged Ethernet port) - one VLAN per PW.
  Each VLAN (logical interface) is the attachment circuit (AC) of the PW.
  There is no MPLS-labeled traffic on the trunk.
  L2 VPNs in either domain - could be PW or VPLS.
P-1
PE-1
P-2
PE-2
SP 1
SP 2
VPN B
Site 1
ASBR-1
ASBR-2
VPN A
Site 1
VPN A
Site 2
VPN B
Site 2
VPN C
Site 1
VPN C
Site 2
IEEE 802.1Q
TRUNK
ONE VLAN
per each PW AC
Pseudo Wires
Pseudo Wires

## Slide 56: Inter-AS PW Stitching - Configuration Excerpts
interfaces {
ge-0/0/9 {
description "private99: mm1 -- mm3";
flexible-vlan-tagging;
encapsulation flexible-ethernet-services;
unit 110 {
vlan-id 110;
encapsulation vlan-ccc;
family ccc;
}
unit 120 {
vlan-id 120;
encapsulation vlan-ccc;
family ccc;
}
...
}
}
protocols {
l2circuit {
neighbor 100.0.0.1 { # PE-1
interface ge-0/0/9.110 {
virtual-circuit-id 1110;
no-control-word;
encapsulation ethernet;
}
interface ge-0/0/9.110 {
virtual-circuit-id 1120;
no-control-word;
encapsulation ethernet;
}
}
neighbor 100.0.0.2 { # PE-2
interface ... { ... }
}
...
}
}

## Slide 57: L2 VPN Stitching - Problem (Loops!)
Problem - L2 loops!
Must be mitigated using some additional mechanisms, such as STP.
Doesn't scale too well.
STP configuration turns into an administrative nightmare.
AS100
AS200
PE-1
PE-2
CE-1
CE-2
ASBR-1a
ASBR-1b
ASBR-2a
ASBR-2b

## Slide 58: Inter-AS L2 VPN - Option C ("Seamless MPLS")
Basic Idea - E2E LSP among all PEs in both SP-1 and SP-2 networks!
Seamless MPLS transport - E2E LSPs signaled using EBGP-LU between ASBRs
VPN signaling - provided by MP-EBGP (multihop) sessions between RRs
P-1
PE-1
P-2
PE-2
SP 1
SP 2
VPN B
Site 1
ASBR-1
ASBR-2
VPN A
Site 1
VPN A
Site 2
VPN B
Site 2
VPN C
Site 1
VPN C
Site 2
EBGP-LU
AFI=1 / SAFI=4
E2E LSP
(signaled by EBGP-LU)
Pseudowire built using
E2E T-LDP session

## Slide 59: Inter-AS PW Over E2E LSPs ("Seamless MPLS")
ASBR-ASBR - uses BGP-LU session (identical to Inter-AS Option C)
PE-PE pseudowire configuration - as follows:
# - PE1
interfaces {
ge-0/0/1 {
description "private0: pe1 -- ce1";
flexible-vlan-tagging;
encapsulation flexible-ethernet-services;
unit 2023 {
vlan-id 2023;
encapsulation vlan-ccc;
family ccc;
}
}
}
protocols {
l2circuit {
neighbor 200.0.0.5 { # PE-5 @ AS200
interface ge-0/0/1.2023 {
virtual-circuit-id 4051431;
no-control-word;
encapsulation ethernet;
}
}
}
}

## Slide 60: E2E L2VPN LSPs - Advantage
E2E LSPs are BGP-controlled.
Thus, all BGP mechanisms / attributes can be used to steer traffic (LP, MED etc.)
AS100
AS200
PE-1
PE-2
CE-1
CE-2
ASBR-1a
ASBR-1b
ASBR-2a
ASBR-2b
BGP-LU
LP=100 (active)
BGP-LU
LP=50 (backup)